Gravity inversion
in spherical coordinates
using tesseroids
Leonardo Uieda
Valéria C. F. Barbosa

---
Cartesian
Spherical
vs

---
Inversion with tesseroids
(Chaves and Ussami, 2013)
- Geoid height anomalies
- Space domain
- Regularization:
  - Depth-weighted Minimum Volume
  - Similarity to seismic tomography

---
Adapt
Planting anomalous densities
(Uieda and Barbosa, 2012)

---
Planting anomalous densities
- Space domain
- Multicomponent: gravity + gradients
- Non-conventional inversion
  - Growth algorithm
  - No linear systems
  - Efficient sensitivity computations

---
Seed

---
Synthetics
- Possible applications
- Advantages
- Shortcomings

---
(Hypothetical) Mantle Plume
Inspired by synthetics in Chaves and Ussami (2013)

---
After Chaves and Ussami (2013)

---
top=100 km
2º
200 km
-50 kg.m-3
700 km

---
gzz at 250 km

---
Seed

---
Joint gz + gzz?

---
Same seed

---
gzz
gz

---
gzz
Joint

---
Lineament with dense rocks (magmatic)
Inspired by Chad lineament model
(Braitenberg et al, 2011)

---
After Braitenberg et al (2011)

---
After Braitenberg et al (2011)

---
top=1 km
8km
10º
N
300 kg.m-3
2º

---
gzz
At 20 km

---
Seeds

---
observed
predicted

---
What if height=120 km?

---
at 20 km
at 120 km

---
observed
predicted

---
at 20 km
at 120 km

---
Even higher
height=270 km

---
at 120 km
at 270 km

---
observed
predicted

---
at 120 km
at 270 km

---
Magmatic underplating
Inspired by model of the Paraná basin
by Mariani et al (2013)

---
After Mariani et al (2013)

---
After Mariani et al (2013)

---
top=30 km
10º
10º
5º
15
km
N
200 kg.m-3

---
gzz at 250 km

---
Seed

---
What if I use wrong density?

---
250 kg.m-3
150 kg.m-3

---
In conclusion

---
OPEN SOURCE
fatiando.org
github.com/leouieda/egu2014